## Slide 1: In-network Angle Approximation for Supporting Adaptive Beamforming
Hiba Mallouhi*, Jaspreet Kaur**, Hasan Tahir Abbas**, Sándor Laki*
* ELTE Eötvös Loránd University, Budapest, Hungary
** University of Glasgow, Glasgow, United Kingdom

## Slide 2: Beamforming
mmWave transmission in 5G
  High propagation loss, signal blockage
  Reduced distance
Beamforming
  Extended communication range
  Enhanced signal quality
  Many advantages…
Beamforming direction is challenging
  BS needs to determine the DOA of its users
  Scanning-like approaches has high energy consumption
  Other techniques has high computational complexities

## Slide 3: An User-Assisted Approach
UE reports it’s location
  based on GPS or other sources
Processing inside the AAN
  Messages handled as control packets
P4 switch assumption
  Angle computation (or distance, etc.)
  Generate configuration message to be sent to the BS
BS reconfigures the beam
  According to new angle (and other) information

## Slide 4: Angle computation is simple
UE coordinates: loc.x, loc.y
BS coordinates: bs.x, bs.y

## Slide 5: Angle computation is simple
UE coordinates: loc.x, loc.y
BS coordinates: bs.x, bs.y
…but, in P4?

## Slide 6: In P4? Preparation
Assuming Tofino-like capabilities
  Constrained hardware
  Pipeline packet processing with lookup tables
Location message from a UE
  Special header format, coordinates and BS id
BS locations stored in a lookup table
  Mapping BS id to coordinates
Absolute value of location difference and the sign of the difference
  The signs determines the quarter around the BS

## Slide 7: In P4? Computing arctan
Goal:
Grid-based approximation with exponential binning
The grid points on both axes are the same:
0, 𝐵1 , 𝐵2 , . . . , 𝐵𝑁 = 𝐷,
  where 𝐵 is the base number,
  𝑁 is the granularity factor (the number of bins on the axes)
  while 𝐷 is the cell diameter (the maximum range)
  Approx. based on the centroid point of the containing grid-cell

## Slide 8: In P4? Computing arctan
Goal:
Grid-based approximation with exponential binning
The grid points on both axes are the same:
0, 𝐵1 , 𝐵2 , . . . , 𝐵𝑁 = 𝐷,
  where 𝐵 is the base number,
  𝑁 is the granularity factor (the number of bins on the axes)
  while 𝐷 is the cell diameter (the maximum range)
  Approx. based on the centroid point of the containing grid-cell
Few properties
Desired accuracy determines the required TCAM space
Other parameters like power, signal strength can similarly be added in the future...
Customization of the table is also possible

## Slide 9: In P4? Final angle transformation
Signs determine the quadrant

## Slide 10: In P4? The whole pipeline
Implemented on Tofino-1 ASIC
Theoretical bound on the angle approximation accuracy
Accuracy vs TCAM space

## Slide 11: Evaluation Approximation Error in static scenarios
Various cell diameters (D): 200-1000 meters
Various numbers of bins (N): 20-80

## Slide 12: Evaluation Moving UE and control latency
UE moving at a constant speed
Control cycle
  time from sending a location message to the reconfiguration of the beam at the BS
P4 switch
Loc msg
Control msg

## Slide 13: Evaluation Moving UE and control latency
UE moving at a constant speed
Control cycle
  time from sending a location message to the reconfiguration of the beam at the BS
P4 switch
Additional error

## Slide 14: Evaluation Moving UE and control latency
UE’s speed: 5-200 kmph
Control cycle: 5-100ms
Simulation
Number of bins (N): 20
Diameter fixed: 800m

## Slide 15: Evaluation Moving UE and control latency
UE’s speed: 5-200 kmph
Control cycle: 5-100ms
Simulation
Number of bins (N): 80
Diameter fixed: 800m

## Slide 16: Evaluation Cost of accuracy
Predictable TCAM size
  And stage number
Low SRAM usage

## Slide 17: Conclusion & Future plans
In-network solutions results in low latency replies
Angle computation is complex but can be approximated
  Bound on the accuracy
Requires moderate per-stage resources
  Possibility to co-locate with other pipelines like 5G-UPF
Integration with a realistic radio propagation simulator
  to quantify the effect of our method on channel quality
Efficient customization of angle prediction table
  E.g., considering BS profiles